## Slide 1: Schematic to GDS SAR Digital Logic CND211 Final Project

## Slide 2: Agenda
This presentation shows our final project submission for
CND211

## Slide 3: Agenda
SAR ADC Logic: From schematic, to GDS.

## Slide 4: SAR ADC
Finds the digital value by binary searching every possible value.

## Slide 5: SAR ADC
Successively approximates the result, bit by bit.

## Slide 6: Our Work

## Slide 10: Our Work

## Slide 11: Our Work

## Slide 12: Our Work

## Slide 13: Our Work

## Slide 14: Our Work
Understanding The Design
Writing the RTL in
SystemVerilog
Making a class-based testing environment.
Synthesis using Design Compiler
Linting using SpyGlass
Formal Verification using Formality
ASIC Flow using
IC Compiler II

## Slide 15: Our Work
Writing the RTL in
SystemVerilog
Making a class-based testing environment.
Synthesis using Design Compiler
Linting using SpyGlass
Formal Verification using Formality
ASIC Flow using
IC Compiler II
Understanding The Design

## Slide 16: Understanding The Design

## Slide 17: Understanding The Design
Scott, M. D., Boser, B. E., & Pister, K.
An ultra-low energy ADC for Smart Dust.

## Slide 18
Scott, M. D., Boser, B. E., & Pister, K.
An ultra-low energy ADC for Smart Dust.

## Slide 19
Scott, M. D., Boser, B. E., & Pister, K.
An ultra-low energy ADC for Smart Dust.

## Slide 20
Scott, M. D., Boser, B. E., & Pister, K.
An ultra-low energy ADC for Smart Dust.

## Slide 21: Our Work
Understanding The Design
Making a class-based testing environment.
Synthesis using Design Compiler
Linting using SpyGlass
Formal Verification using Formality
ASIC Flow using
IC Compiler II
Writing the RTL in
SystemVerilog

## Slide 22: Writing the RTL in SystemVerilog

## Slide 23: Writing the RTL in SystemVerilog
Two modules were implemented:

## Slide 24: Writing the RTL in SystemVerilog
Two modules were implemented:
Set Propagator
SAR Custom Register

## Slide 25: Writing the RTL in SystemVerilog
Design is generic. The resolution, 10 bits, is a parameter.

## Slide 26: Our Work
Understanding The Design
Writing the RTL in
SystemVerilog
Synthesis using Design Compiler
Linting using SpyGlass
Formal Verification using Formality
ASIC Flow using
IC Compiler II
Making a class-based Testing Environment

## Slide 27: Making a class-based Testing Environment

## Slide 28: Testing Environment

## Slide 29: Testing Environment
Generate a random analog value.

## Slide 30: Testing Environment
Send the analog value to the analog frontend

## Slide 31: Testing Environment
Compare the DUT output with the ADC output.

## Slide 32: Testing Environment

## Slide 33: Testing Environment
Compare the DUT output with the expected output.

## Slide 34: Coverage

## Slide 35: Coverage
The verbose print setting in the transaction class was turned off in the simulation. The code is something like this: if not verbose then return.
Thus the 50% branch coverage .

## Slide 36: Coverage
Same reason for statement coverage (87.5%)

## Slide 37: Coverage
Other than that, everything is at an acceptable percentage.

## Slide 38: Our Work
Understanding The Design
Writing the RTL in
SystemVerilog
Making a class-based testing environment
Synthesis using Design Compiler
Formal Verification using Formality
ASIC Flow using
IC Compiler II
Linting using SpyGlass

## Slide 39: Linting using SpyGlass

## Slide 40: Linting using SpyGlass
The paper contains many un-orthodox techniques.

## Slide 41
SpyGlass was annoyed at the core principles of the design.

## Slide 43
Clock connected to zero : Linting Error

## Slide 44
Flipflop clocks are outputs of other flipflops: Linting Error

## Slide 45
Async set pins of flipflops are outputs of other flipflops: Linting Error

## Slide 46: All these errors can be waived
These are core design principles of the SAR ADC.

## Slide 47: Our Work
Understanding The Design
Writing the RTL in
SystemVerilog
Making a class-based testing environment.
Linting using SpyGlass
Formal Verification using Formality
ASIC Flow using
IC Compiler II
Synthesis using Design Compiler

## Slide 48: Synthesis using Design Compiler

## Slide 49: Synthesis
Requirements
10 Bit SAR ADC.
100 MS/s 1.1 GHz
Using SAED90nm

## Slide 50: Synthesis
Use LVT cells for performance (Sacrifice Power).

## Slide 51: Corners
MAX Corner
125
0.65 Volts

## Slide 52: Corners
MAX Corner
125
0.65 Volts
MIN Corner
-40
0.9 Volts

## Slide 53: Timing Report

## Slide 54: Timing Report

## Slide 55: Critical Path Report

## Slide 56: Although small, more performance can be “squeezed” from the design.

## Slide 57: Our Work
Understanding The Design
Writing the RTL in
SystemVerilog
Making a class-based testing environment.
Synthesis using Design Compiler
ASIC Flow using
IC Compiler II
Linting using SpyGlass
Formal Verification using Formality

## Slide 58: Formal Verification using Formality

## Slide 59: Formal Verification

## Slide 60: Formal Verification

## Slide 61: A Latch?
The design contains no latches.
Design compiler did not warn about unintentional latches being inferred.
The generated netlist does not contain any latch cell.

## Slide 62: A Latch?
Reference
Implementation

## Slide 63: A Latch?
Reference
Implementation
No clock in reference!

## Slide 64: A Latch?
Reference
Implementation
Implementation has a clock pin, is a normal DFF.

## Slide 65: The code in question
always_ff @(posedge dummy_ground, negedge i_rstn, negedge i_setn[0]) begin
if (~i_setn[0]) sar_reg_out[0] <= 1'b1;
else if (~i_rstn) sar_reg_out[0] <= 1'b0;
else sar_reg_out[0] <= 1'b0;
end

## Slide 66: Explanation
A DFF with asynchronous set / reset

## Slide 67: Explanation
With the clock and D connected to zero…

## Slide 68: Explanation
Behaves like an SR latch.

## Slide 69: Explanation
DC recognized the always_ff and did not infer a latch.

## Slide 70: Explanation
Formality, however, inferred a latch.

## Slide 71: Explanation

## Slide 72: Explanation

## Slide 73: Our Work
Understanding The Design
Writing the RTL in
SystemVerilog
Making a class-based testing environment.
Synthesis using Design Compiler
Linting using SpyGlass
Formal Verification using Formality
ASIC Flow using
IC Compiler II

## Slide 74: ASIC Flow using IC Compiler II
Understanding The Design
Writing the RTL in
SystemVerilog
Making a class-based testing environment.
Synthesis using Design Compiler
Linting using SpyGlass
Formal Verification using Formality

## Slide 75: Preparing the NDM
Was smooth sailing, except…

## Slide 76: Preparing the NDM
Two cells in the .lef file had incorrect dimensions.

## Slide 77: Preparing the NDM
The heights were not multiples of the sole site definition in the technology data.

## Slide 78: The Offending Cells
LSDNENCLX4_LVT
LSDNENCLX8_LVT

## Slide 79: The Offending Cells
High to low level shifters with high active enables clamp low.

## Slide 80: The Offending Cells
We are not using any level shifters in the design.

## Slide 81: The Offending Cells
Solution: Remove the level shifters from the lef file.

## Slide 82: Floor And Power Planning
No power ring, as this design will be part of a larger design (in the same chip with the analog front end)

## Slide 83: Placement And CTS
After placement and CTS, the critical path slack has improved by 44%

## Slide 84: After Placement And CTS

## Slide 85: After Routing + Filler Cell Insertion

## Slide 86: After Routing + Filler Cell Insertion

## Slide 87
Final IC

## Slide 88
IR Drop

## Slide 89
Electromigration

## Slide 90: Final Timing (Using PrimeTime)